f_motion = f_rest over {1- u over c}
f_motion = f_rest over {1- u over c}
Physics	LW #10 : Find the speed of a car using the Doppler effect

I. Introduction to the Doppler effect
Lab equipment:	• Acquisition system Sysam SP5 and software Latis Pro
• ultrasound transmitter and receiver

1. Value of the frequency of the transmitter at rest : fRest
Practical work:
• Connect the transmitter (“continuous mode”) to the 12 V power supply of the Sysam SP5 box.
• Connect the receiver to the EA0 entrance of the Sysam SP5.
• Set the receiver in front of the transducer, at a distance of approximately 30 cm.
• Set the acquisition parameters of the software Latis Pro in order to register 10 periods (for remining: the frequency of these ultrasounds are about 40kHz). If necessary, do several acquisitions in order to register an even signal.
Result:
• Use the different methods explained in the instructions of Latis Pro to determine the frequency at rest fRest .

2. The Doppler effect :
• Register a new signal, when the receiver is moved towards the transmitter. It is necessary to set the trigger (“déclenchement”) so that the recording starts when the receiver is about at 20 cm from the transmitter.
• Measure the frequency in motion: fMotion
Relation between
the fréquencies :
Analysis :
• According to your knowledge on the Doppler effect, how will the frequency be modified by the motion? Write down an inequality between frest and fmotion.
• The relation between these two frequencies is given in the adjacent frame, where u is the relative speed between the transmitter and the receiver, and c is the wave velocity.(c=340m/s). Deduce an estimation of the speed u of the receiver in your experiment.
• Does this value seem correct?
II. The principle of a radar speed gun.
A radar speed gun (also radar gun and speed gun) is a device used to measure the speed of moving objects. It is used in law-enforcement to measure the speed of moving vehicles and is often used in professional spectator sport, for things such as the measurement of bowling speeds in cricket, speed of pitched baseballs, athletes and tennis serves.
A Mesta radar speed gun is a Doppler radar unit that uses a 24,150 GHz continuous electromagnetic wave. It measures the speed of the objects at which it is pointed by detecting a change in frequency of the returned radar signal caused by the Doppler effect, whereby the frequency of the returned signal is increased in proportion to the object's speed of approach if the object is approaching, and lowered if the object is receding.
Lab equipment:	• Acquisition system Sysam SP5 and software Latis Pro
• ultrasound transmitter and receiver
• a screen
Practical work:
1. Write down a procedure to measure the speed of a mobile target (the screen) with the Doppler effect.
2. After your teacher checked your procedure, try to do the experiment to find the speed of the screen. The relation is: v = {f_reveiver - f_transmitter} over {2 times f_receiver} times c , c: ultrasound velocity in air.
Note : Why is there a coefficient 2 in this formula?

III. Application de l'effet Doppler en astrophysique
Activité 6 p. 73 sauf question 5
Physics	LW #10 : Find the speed of a car using the Doppler effect

I. Introduction to the Doppler effect
Lab equipment:	• Acquisition system Sysam SP5 and software Latis Pro
• ultrasound transmitter and receiver

1. Value of the frequency of the transmitter at rest : fRest
Practical work:
• Connect the transmitter (“continuous mode”) to the 12 V power supply of the Sysam SP5 box.
• Connect the receiver to the EA0 entrance of the Sysam SP5.
• Set the receiver in front of the transducer, at a distance of approximately 30 cm.
• Set the acquisition parameters of the software Latis Pro in order to register 10 periods (for remining: the frequency of these ultrasounds are about 40kHz). If necessary, do several acquisitions in order to register an even signal.
Result:
• Use the different methods explained in the instructions of Latis Pro to determine the frequency at rest fRest .

2. The Doppler effect :
• Register a new signal, when the receiver is moved towards the transmitter. It is necessary to set the trigger (“déclenchement”) so that the recording starts when the receiver is about at 20 cm from the transmitter.
• Measure the frequency in motion: fMotion
Relation between
the frequencies :
Analysis :
• According to your knowledge on the Doppler effect, how will the frequency be modified by the motion? Write down an inequality between frest and fmotion.
• The relation between these two frequencies is given in the adjacent frame, where u is the relative speed between the transmitter and the receiver, and c is the wave velocity.(c=340m/s). Deduce an estimation of the speed u of the receiver in your experiment.
• Does this value seem correct?
II. The principle of a radar speed gun.
A radar speed gun (also radar gun and speed gun) is a device used to measure the speed of moving objects. It is used in law-enforcement to measure the speed of moving vehicles and is often used in professional spectator sport, for things such as the measurement of bowling speeds in cricket, speed of pitched baseballs, athletes and tennis serves.
A Mesta radar speed gun is a Doppler radar unit that uses a 24,150 GHz continuous electromagnetic wave. It measures the speed of the objects at which it is pointed by detecting a change in frequency of the returned radar signal caused by the Doppler effect, whereby the frequency of the returned signal is increased in proportion to the object's speed of approach if the object is approaching, and lowered if the object is receding.
Lab equipment:	• Acquisition system Sysam SP5 and software Latis Pro
• ultrasound transmitter and receiver
• a screen
Practical work:
1. Write down a procedure to measure the speed of a mobile target (the screen) with the Doppler effect.
2. After your teacher checked your procedure, try to do the experiment to find the speed of the screen. The relation is: v = {f_reveiver - f_transmitter} over {2 times f_receiver} times c , c: ultrasound velocity in air.
Note : Why is there a coefficient 2 in this formula?

III. Application de l'effet Doppler en astrophysique
Activité 6 p. 73 sauf question 5